## Slide 1
Unit 5
Procedure and Macro

## Slide 2
Define procedure : A procedure is group of instructions that usually performs one task. It is a reusable section of a software program which is stored in memory once but can be used as often as necessary.
A procedure can be of two types. 1) Near Procedure 2) Far Procedure
Near Procedure:
A procedure is known as NEAR procedure if is written(defined) in the same code segment which is calling that procedure. Only Instruction Pointer(IP register) contents will be changed in NEAR procedure.
FAR procedure :
A procedure is known as FAR procedure if it is written (defined) in the different code segment than the calling segment. In this case both Instruction Pointer(IP) and the Code Segment(CS) register content will be changed.

## Slide 3
Directives used for procedure :
PROC directive:
The PROC directive is used to identify the start of a procedure. The PROC directive follows a name given to the procedure.
After that the term FAR and NEAR is used to specify the type of the procedure.
ENDP Directive:
This directive is used along with the name of the procedure to indicate the end of a procedure to the assembler.
The PROC and ENDP directive are used to bracket a procedure.

## Slide 4
CALL instruction and RET instruction :
CALL instruction :
The CALL instruction is used to transfer execution to a procedure.
It performs two operation.
When it executes, first it stores the address of instruction after the CALL instruction on the stack .
Second it changes the content of IP register in case of Near call and changes the content of IP register and cs register in case of FAR call.
There are two types of calls
1)Near Call or Intra segment call.
2) Far call or Inter Segment call

## Slide 5
Operation for Near Call :
When 8086 executes a near CALL instruction, it decrements the stack pointer by 2 and copies the IP register contents on to the stack.
Then it copies address of first instruction of called procedure.
SP  SP-2
IP  stores onto stack
IP  starting address of a procedure.

## Slide 6
Operation of FAR CALL:
When 8086 executes a far call, it decrements the stack pointer by 2 and copies the contents of CS register to the stack.
It the decrements the stack pointer by 2 again and copies the content of IP register to the stack.
Finally it loads cs register with base address of segment having procedure and IP with address of first instruction in procedure
SP  SP-2
CS contents  stored on stack
SP  SP-2
IP contents  stored on stack
CS  Base address of segment having procedure
IP  address of first instruction in procedure.

## Slide 7
RET instruction :
The RET instruction will return execution from a procedure to the next instruction after call in the main program.
At the end of every procedure RET instruction must be executed.
Operation for Near Procedure :
For NEAR procedure ,the return is done by replacing the IP register with a address popped off from stack and then SP will be incremented by 2.
IP  Address from top of stack
SP  SP+2
Operation for FAR procedure :
IP register is replaced by address popped off from top of stack, then SP will be incremented by 2.The CS register is replaced with a address popped off from top of stack. Again SP will be incremented by 2.
IP  Address from top of stack
SP  SP+2
CS  Address from top of stack
SP  SP+2